## Slide 1: Spectra of the Moon using a Robotic Telescope
E.Almas, T.Christopherson, W.Hogg, E.Stone

## Slide 2
Goals: the following steps (1-5) are mandatory in order to complete the project, however you may boost marks, either as a group, or as an individual, with optional goals (5-8).
(1)Demonstrate acquiring calibrated test spectra of different materials .g. tarmac, concrete, rock samples, vegetation, using a hand held spectrometer.
(2)Use N (e.g. 20) identifiable reference areas of the Moon (highland and/or mare) to calibrate measured brightness values in the CCD camera wrt a standard lunar pectrum(find this on-line).
(3)select and measure some target areas that you want to measure the spectrum of wrt the previously derived standard lunar spectra.
(4)Analyse the spectra from (3) to determine –can you see any mineral absorption ands –what might these be? What is/are the most colourful area(s)f the Moon?
(5)How accurately can you measure absorption bands in the spectra of lunar surface features you are studying(use propagation of errors)?
(6)Investigate whether the telescope optics suffer from vignetting, or other non-linear sensitivity effects, across the image. Can you calibrate out/mitigate this effect if present?
(7)Experiment with producing meaningful co-registered colour ratio images of the lunar surface o highlight surface composition differences.
(8)Repeat your spectra measurements at other lunar phases to see if the surface changes colour at different illumination and viewing angles?

## Slide 3: Spectra of objects with handheld spectrometer
Chart: Wavelength/nm
| 470 | 555 | 585 | 605 | 635 | 660 | 695 | 880 | 940
Blue(ish) Carpet: | 240 | 278 | 258 | 259 | 250 | 280 | 300 | 280 | 215
Blue pin board: | 260 | 145 | 138 | 130 | 128 | 213 | 209 | 524 | 354
Green fabric pin board: | 163 | 252 | 165 | 137 | 133 | 181 | 189 | 369 | 256
Leaf: | 151 | 280 | 211 | 165 | 123 | 249 | 412 | 615 | 405
Green sheet of paper: | 355 | 690 | 463 | 385 | 367 | 510 | 634 | 900 | 577
Yellow book cover: | 393 | 1221 | 1219 | 1134 | 1119 | 1250 | 1353 | 1195 | 692
Yellow sheet of papir: | 387 | 1242 | 1222 | 1104 | 1084 | 1199 | 1271 | 1050 | 644
Red book cover: | 211 | 234 | 374 | 520 | 602 | 719 | 804 | 765 | 465
Cardboard: | 331 | 550 | 575 | 532 | 510 | 608 | 72 | 623 | 395
Stone (smooth): | 198 | 252 | 230 | 147 | 227 | 253 | 247 | 190 | 140
Stone (rough): | 266 | 353 | 321 | 256 | 225 | 271 | 279 | 220 | 158
White paint: | 1056 | 1125 | 1030 | 1017 | 983 | 1075 | 1200 | 1040 | 593

## Slide 4: Comparing to Known spectra
Chart: 
| 470 | 555 | 585 | 605 | 635 | 660 | 695 | 880 | 940
Leaf: | 151 | 280 | 211 | 165 | 123 | 249 | 412 | 615 | 405
Figure 1: Mean reflectance spectra of brown leaf litter (n = 20) and... - Scientific Figure on ResearchGate. Available from: https://www.researchgate.net/figure/276212092_fig6_Figure-1-Mean-reflectance-spectra-of-brown-leaf-litter-n-20-and-green-foliage-n [accessed Feb 19, 2016]