## Slide 1: Spectra of the Moon using a Robotic Telescope
E.Almas, T.Christoffersen, W.Hogg, E.Stone

## Slide 2
Goals: the following steps (1-5) are mandatory in order to complete the project, however you may boost marks, either as a group, or as an individual, with optional goals (5-8).
(1)Demonstrate acquiring calibrated test spectra of different materials .g. tarmac, concrete, rock samples, vegetation, using a hand held spectrometer.
(2)Use N (e.g. 20) identifiable reference areas of the Moon (highland and/or mare) to calibrate measured brightness values in the CCD camera wrt a standard lunar pectrum(find this on-line).
(3)select and measure some target areas that you want to measure the spectrum of wrt the previously derived standard lunar spectra.
(4)Analyse the spectra from (3) to determine –can you see any mineral absorption ands –what might these be? What is/are the most colourful area(s)f the Moon?
(5)How accurately can you measure absorption bands in the spectra of lunar surface features you are studying(use propagation of errors)?
(6)Investigate whether the telescope optics suffer from vignetting, or other non-linear sensitivity effects, across the image. Can you calibrate out/mitigate this effect if present?
(7)Experiment with producing meaningful co-registered colour ratio images of the lunar surface o highlight surface composition differences.
(8)Repeat your spectra measurements at other lunar phases to see if the surface changes colour at different illumination and viewing angles?

## Slide 3: Spectra of objects with handheld spectrometer
Chart: Wavelength/nm
| 470 | 555 | 585 | 605 | 635 | 660 | 695 | 880 | 940
Blue(ish) Carpet: | 12 | 13.9 | 12.9 | 12.95 | 12.5 | 14 | 15 | 14 | 10.75
Blue pin board: | 13 | 7.25 | 6.9 | 6.5 | 6.4 | 10.65 | 10.45 | 26.2 | 17.7
Green fabric pin board: | 8.15 | 12.6 | 8.25 | 6.85 | 6.65 | 9.05 | 9.45 | 18.45 | 12.8
Leaf: | 7.55 | 14 | 10.55 | 8.25 | 6.15 | 12.45 | 20.6 | 30.75 | 20.25
Green sheet of paper: | 17.75 | 34.5 | 23.15 | 19.25 | 18.35 | 25.5 | 31.7 | 45 | 28.85
Yellow book cover: | 19.65 | 61.05 | 60.95 | 56.7 | 55.95 | 62.5 | 67.65 | 59.75 | 34.6
Yellow sheet of papir: | 19.35 | 62.1 | 61.1 | 55.2 | 54.2 | 59.95 | 63.55 | 52.5 | 32.2
Red book cover: | 10.55 | 11.7 | 18.7 | 26 | 30.1 | 35.95 | 40.2 | 38.25 | 23.25
Cardboard: | 16.55 | 27.5 | 28.75 | 26.6 | 25.5 | 30.4 | 3.6 | 31.15 | 19.75
Stone (smooth): | 9.9 | 12.6 | 11.5 | 7.35 | 11.35 | 12.65 | 12.35 | 9.5 | 7
Stone (rough): | 13.3 | 17.65 | 16.05 | 12.8 | 11.25 | 13.55 | 13.95 | 11 | 7.9
White paint: | 52.8 | 56.25 | 51.5 | 50.85 | 49.15 | 53.75 | 60 | 52 | 29.65

## Slide 4: Calibrating the Spectrometer
“Before analysing a sample it is frequently necessary to check the calibration of the spectrometer that is being used. This is performed by analysing known samples and measuring the error between the empirical and known values for the samples. A skew, or bias, can be introduced into the data handling routines of the data analysis equipment of the spectrometer to compensate for these differences.”
Davies, Anthony MC, and Harald A. Martens. "Method and apparatus for calibrating a spectrometer." U.S. Patent No. 5,321,970. 21 Jun. 1994.

## Slide 5: Comparing to Known spectra
Chart: 
| 470 | 555 | 585 | 605 | 635 | 660 | 695 | 880 | 940
Leaf: | 7.55 | 14 | 10.55 | 8.25 | 6.15 | 12.45 | 20.6 | 30.75 | 20.25
Figure 1: Mean reflectance spectra of brown leaf litter (n = 20) and... - Scientific Figure on ResearchGate. Available from: https://www.researchgate.net/figure/276212092_fig6_Figure-1-Mean-reflectance-spectra-of-brown-leaf-litter-n-20-and-green-foliage-n [accessed Feb 19, 2016]
http://speclab.cr.usgs.gov/PAPERS.refl-mrs/refl4.html#section4.3
Only leaf has a good spectrum for comparison
(other materials are too generic to find data for)

## Slide 6: Comparing to Known spectra
Chart: 
| 470 | 555 | 585 | 605 | 635 | 660 | 695 | 880 | 940
Leaf: | 7.55 | 14 | 10.55 | 8.25 | 6.15 | 12.45 | 20.6 | 30.75 | 20.25
Figure 1: Mean reflectance spectra of brown leaf litter (n = 20) and... - Scientific Figure on ResearchGate. Available from: https://www.researchgate.net/figure/276212092_fig6_Figure-1-Mean-reflectance-spectra-of-brown-leaf-litter-n-20-and-green-foliage-n [accessed Feb 19, 2016]
http://speclab.cr.usgs.gov/PAPERS.refl-mrs/refl4.html#section4.3
Couldn’t find data values, and can’t read from these graphs, so calibrating our data wasn’t possible here

## Slide 7: Planning with the weather and lunar-tables
http://www.metoffice.gov.uk/public/weather/forecast/gcm45jgg9#?fcTime=1456185600
http://www.moonconnection.com/moon_phases_calendar.phtml

## Slide 8: Taking our own images

## Slide 10: Tony’s Images (2013)
436nm
589nm
656nm
730nm
855nm

## Slide 11: Using Tony’s Images
R-Band of Mare Serenitatis, top center of image, and Mare Tranquillitatis, right.
436nm
589nm
656nm
730nm
855nm
Only small area of these images where images aren’t saturated or suffering from other effects (Tom, any other reason?)

## Slide 12: False Colour Imaging
Combined the images to create RGB image where:
Red represents I-band,
Green representing R-band
Blue representing B-band
Other bands were too blurry or were saturated

## Slide 13
Comparing this to NASAs spectral composition of the moon shows a similar result where Mare Serenitatis is in the green-yellow part of the spectrum and Mare Tranquillitatis is in the blue-purple part.

## Slide 15
JOURNAL OF GEOPHYSICAL RESEARCH, VOL. 101, NO. El0, PAGES 23,213-23,228, OCTOBER 25, 1996
41stLunarandPlanetaryScienceConference(2010), http://www.lpi.usra.edu/meetings/lpsc2010/pdf/2494.pdf
Chart: Mare Tranquillitatis & Serenitatis Albedo Spectra
| 436 | 589 | 656 | 730 | 855
Tranquillitatis | 0.67843 | 0.69804 | 0.67451 | 0.54902 | 0.58039
Seneritatis | 0.6 | 0.57647 | 0.62157 | 0.41176 | 0.50588
Mare
Tranquillitatis
Mare
Serenitatis
Comparing to known spectra

## Slide 16: Comparing Different mare and highland
This is where i want ur stuffs tome, histogram comperson

## Slide 17: Mineral Absorption Bands
Chart: Mare Tranquillitatis & Serenitatis Albedo Spectra
| 436 | 589 | 656 | 730 | 855
Tranquillitatis | 0.67843 | 0.69804 | 0.67451 | 0.54902 | 0.58039
Seneritatis | 0.6 | 0.57647 | 0.62157 | 0.41176 | 0.50588
Mare
Tranquillitatis
Mare
Serenitatis
http://speclab.cr.usgs.gov/PAPERS.refl-mrs/refl4.html

## Slide 18: Mineral Absorption Bands
Chart: Mare Tranquillitatis & Serenitatis Albedo Spectra
| 436 | 589 | 656 | 730 | 855
Tranquillitatis | 0.67843 | 0.69804 | 0.67451 | 0.54902 | 0.58039
Seneritatis | 0.6 | 0.57647 | 0.62157 | 0.41176 | 0.50588
Mare
Tranquillitatis
Mare
Serenitatis
Both contain pyroxene (though can’t determine grain size)
Mare Serenitatis probably contains Fo 29
http://speclab.cr.usgs.gov/PAPERS.refl-mrs/refl4.html

## Slide 19: How accurately can we measure the absorption bands in the spectra?
Depends on calibration of scope, therefore very hard to determine.
By taking into account the following affects we can reduce errors

## Slide 20: Optical effects:
Vignetting:
Effect that darkens the corners of a picture
(ask tom if noticable when creating moeacs)’
Flat-fiel images
Also removes any dust rings
«Toms picture of Tonys dust rings»

## Slide 21
Vignetting Examples:

## Slide 22: Correcting images

## Slide 23: No vignetting and much sharper

## Slide 24: Chromatic aberration
Happens in poorly made lenses
Depends on Reflective indices
Seen in strong contrast
Effects are probably negligable in this experiment
https://en.wikipedia.org/wiki/Chromatic_aberration

## Slide 25: Clouds/Atmospheric Effects
In the first set of our images, can see the effects of clouds (the darker patch)
Even without clouds our atmosphere will affect our images

## Slide 26: When taking raw pictures
Remember disclaimer to say we have not calibrated our pictures:
(Tom’s pictures and graphs that take into account earth’s atmosphere, as it will effect absorption bands)
Light pollution also needs to be taken into account(clearer sky)